## Slide 1: How GPUs Work?

## Slide 2: OUTLINE
An overview of graphics rendering pipeline
An overview of graphics programming
An overview of GPU architecture - three main ideas behind GPU architecture

## Slide 3
Part - 1
An overview of graphics rendering pipeline

## Slide 4: The Graphics Rendering Pipeline
Rendering
  Process to convert high level description to a specific instance
Graphics Rendering
  Process to convert raw 3D scene description (set of vertices) to a 2D pixel image
Graphics Rendering Pipeline
  Sequence of stages followed during graphics rendering process

## Slide 5: Main Stages In Graphics Rendering Pipeline
Vertex Processing
Primitive Processing
Fragment Processing
  transform input vertices from world space to screen space
  apply texture to vertices
  convert set of vertices to set of primitives (usually triangles)
  remove (part of) primitives which lie outside the screen space
  3D to 2D coordinate mapping of all primitive units
  find all the fragments (pixels) which belong to each primitive unit
  apply different attributes like color, lighting, texture, etc to fragments

## Slide 6: Graphics Rendering Pipeline - An Illustration
Vertex Processing
Set of Vertices

## Slide 7: Graphics Rendering Pipeline - An Illustration
Primitive Processing
Primitives
Fragments

## Slide 8: Graphics Rendering Pipeline - An Illustration
Fragment Processing
Shaded Fragments
Pixels

## Slide 10
Part - 2
An Overview of Graphics Programming

## Slide 11: Graphics Programming - Key Observations
Vertex Processing
Primitive Processing
Fragment Processing
Each vertex can be programmed independently, and same sequence of vertex operations is applied to each vertex
Each primitive can be programmed independently, and same sequence of primitive operations is applied to each primitive
Each fragment can be programmed independently, and same sequence of fragment operations is applied to each fragment
Scope for massive parallelism
SPMD (Single Program Multiple Data) parallelism
Hardware can be designed by keeping this massive parallelism in mind, and programmable GPUs were initially born this way
Corresponding programming model is called shader programming model

## Slide 12: How Shader Programming Works? Shader Compilation
A fragment shader
Compiled fragment shader
Shader Compiler

## Slide 13: How Shader Programming Works? Shader Execution
Shader execution

## Slide 14
Part - 3
An Overview of GPU Architecture
How GPUs Can Be Designed To Take Advantage Of Massive Parallelism?

## Slide 15: CPU-Style Cores
CPU-style cores
Makes sequential program execution faster

## Slide 16: Idea #1: Slim Down The Core And Pack Multiple Simple Cores

## Slide 19
16 cores = 16 copies of same simultaneous instruction streams,
but, each work on 16 different fragment data to produce corresponding output fragment

## Slide 20: Idea #2: Pack More ALUs Within The Core (SIMD Processing)
SIMD Processing
Single Instruction Multiple Data

## Slide 21
New Modified Shader
vector instructions

## Slide 22
Type to enter a caption.

## Slide 23
So Far So Good!
But, what about Stalls which occurs because of instruction dependency?
We have removed fancy Caches and Logic which avoid stalls to a greater extent in CPU-style cores.

## Slide 25: Idea #3: Hide Latency To Achieve Maximum Throughput
We have LOTS of independent fragments.
(way more fragments to process than ALUs)
Interleave processing of many fragments on a single core to avoid stalls caused by high latency operations.
In Layman words, keep the cores always busy, and it is possible to a greater extent in graphics programming.

## Slide 29
Our Example GPU
Idea #1: 16 cores per chip (SPMD at chip level)
Idea #2: 8 ALUs per core (SIMD at core level)
Idea #3: 4 execution contexts per core (in order to
hide latency)
So, at any given point of time, processing of 512 concurrent fragments are in flight!
Todays modern GPUs are a way more powerful than this illustrated example GPU!

## Slide 30
Questions?